Analytical overview of approaches to modeling the oxygen-induced cracking processes

Filipp S. Sovetin

Associate professor (docent) of Department of Computer Science & Computer Aided Design (CAD). D.I. Mendeleyev University of Chemical Technology of Russia. Address: Russia, 125047 Moscow 9 Miusskaya square

E-mail: fsovetin@inbox.lv  Tel. +7(499)-978-84-18, +7(499)-500-19-17

Yliya I. Gordievskaya

The undergraduate of Department of Computer Science & Computer Aided Design (CAD). D.I. Mendeleyev University of Chemical Technology of Russia.

Address: Russia, 125047 Moscow 9 Miusskaya square.

E-mail: jg0311@bk.ru

Tamas N. Gartman

The director of Department of Computer Science & Computer Aided Design (CAD). D.I. Mendeleyev University of Chemical Technology of Russia.

Address: Russia, 125047 Moscow 9 Miusskaya square

E-mail: gartman@muctr.ru. Tel. +7(499)-978-84-11

Dina K. Novikova

Associate professor (docent) of Department of Computer Science & Computer Aided Design (CAD). D.I. Mendeleyev University of Chemical Technology of Russia. Address: Russia, 125047 Moscow 9 Miusskaya square

E-mail: novidin@yandex.ru

Tel.  +7(499)-978-84-18

Keywords: modeling, cracking, reactor, mathematical model, system of equations.

Analytical overview of the existing approaches to computer modeling the oxygen-induced cracking processes was performed. The chemical schemes and kinetic modeling techniques the oxygen-induced tar cracking processes, methods of mathematical modeling including representation of chemical reactions for the components groups and taking into account the reactions based on the model components, modeling of the dynamic mode of the process based on the concept of predictive control have been studied. Based on the analysis it was found that for the modeling of this process it is advisable to choose the model components that are the most informative to characterize the properties of fractions and use them for the compilation of balance equations.

References

1.  Zolotuhin V. A. Deep processing of heavy oil and oil residues // Sfera Neftegaz [Field of Oil and Gas]. no. 4. 2012. pp. 70-75. (in Russ).

2. Gartman T.N, Sovetin F. S., Proskuro E. A., Shvets V. F., Kozlovskiy R. A., Suchkov Y.P, Sapunov V.N., Loktev A. S., Levchenko D. A., Dedov A.G. Computation of the Solid Catalyzed Gas Phase Reactions with a Simultaneous Choice of the Scheme of the Reactions for Different Composition of the Initial Reaction Mixture // Chemical engineering transactions. Vol. 39. 2014. pp.1009-1014.

3. Suchkov Yu.P.,  Kozlovskii R.A.,  Shvec V.F.,  Gorbunov A.V.,  Luganskii A.I. A method of thermal-oxidative cracking of heavy oil residues // Butlerovskie soobscheniya [Butlerov Communications]. 2014. Т. 37. no. 2. pp. 60-65. (in Russ).

4.  Shvec V.F., Suchkov Yu.P., Kozlovskii R.A., Luganskii A.I.,  Gorbunov A.V. Thermo-oxidative cracking fuel oil. Investigation of the process flow reactor // Himicheskaya promishlennost segodnya [Chemical Industry Today]. 2013. no 10. pp. 19-25.  (in Russ).

5. Shvec V. F., Sapunov V. N., Kozlovskii R.A., Makarov M. G., Gartman T. N.,

Luganskii A. I., Sovetin F. S.,  Suchkov Yu. P., Gorbunov A. V. Some embodiments of the deepening of oil refining // Jurnal prikladnoi himii [Journal of Applied Chemistry]. Т. 89, no. 11. 2016. pp. 114-125. (in Russ).

6. Hanikyan V.L.,  Litvincev I. Yu.,  Shvec V. F., Moroz I. V. i dr. Deep thermal cracking of heavy oil residues, initiated by ozone // Himicheskaya promishlennost segodnya [Chemical Industry Today]. 2004. no.12. pp.31-40. (in Russian).

7. Galiev R. G., Luganskii A. I., Tretyakov V.F., Ermakov A.N. Initiating the process thermal cracking of heavy oil residues by atmospheric oxygen // Mir nefteproduktov. Vestnik neftyanih kompanii. [World oil products. Bulletin of the oil companies.] 2007. no. 8. pp. 16-19.  (in Russ).

8. Galiev R. G., Luganskii A. I., Moroz I. V., Ermakov A. N. Justification activation mechanism of tar thermal cracking atmospheric oxygen // Mir nefteproduktov. Vestnik neftyanih kompanii. [World oil products. Bulletin of the oil companies.]. 2008. no. 7. pp. 16-19. (in Russ).

9. Vorobev Yu.V., Kuzmin A.P. Chemical processes in organic liquids initiated hydrodynamic activator // Vestnik Tambovskogo gosudarstvennogo tehnicheskogo universiteta. [Journal of Tambov State Technical University]. 2012. t. 18. no. 4. pp. 905-911. (in Russ).

10. Petrov A.A., Balyan H.V., Troschenko A.T., Organic chemistry. 2002. 624 pp. (in Russ).

11. Pivovarova M. A., Tumanyan B. P., Belinskii B. I. Vibskreking oilstock. M.: « Tehnika ». 2002. 64 pp. (in Russ).

12. Mircea C., Agachi S., Marimoiu V. Simulation and Model Predictive Control of a Universal Oil Products Fluid Catalytic Cracking // Chemical Engineering and Processing. 2003. V. 42.  pp. 67-91.

13. Pashaeva B.A. Synthesis catalytic oil cracking process control system using a predictive model  // Injenernii vestnik Dona [Engineers Don Gazette]. 2013. t. 24. no. 1 (24). pp. 12-21. (in Russ).

14. Jiarui Z., Zhiqing W., Hao J., Jizheng C., Jing Zh., Shuai Sh.. Modeling fluid catalytic cracking risers with special pseudo-components // Chemical Engineering Science 2013. V.102, no. 10, pp. 87–98.

15. Goncharov D. V.  Small reactor thermal-oxidative process of cracking a hydrocarbon liquid fuel. Dissertation :  05.17.08. M. MSUEE (MIHM). 2005. (in Russ).

16.  Pashaeva B.A., Farhadov M.P. Management based on predictive models in the catalytic cracking of petroleum systems //  Vestnik Voronejskogo gosudarstvennogo tehnicheskogo universiteta [Journal of Voronezh State Technical University.]. 2013. t. 9. no. 2. pp. 33-36. (in Russ).

17. Ahmadova H.H.,  Abdulmejidova Z.A.,  Kadiev H.M., Sirkin A.M. Application vibskrekinga processes in the composition of the combined schemes of oil refining // Elektronnii nauchnii jurnal  « Neftegazovoe delo ». [Electronic journal « Oil and gas business»] 2011. no.2. pp. 103-115. (in Russ).

18. Yaroschuk L. D., Bondarenko Yu. G., Goncharenko S. N. Simulation modeling of catalytic cracking processes // Prikaspiiskii jurnal: upravlenie i visokie tehnologii. [Caspian journal : management and high technology]. no. 1 (25). 2014. pp. 46-58. (in Russ).

19. Bequette W. Process Control Modeling Desing and Simulation - Pretice Hall

PTTr. 2003.  564 pp.

20. Coleman B., Babu J. Techniques of Model–Based Control - Pretice Hall PTTr.

2002.  576 pp.

21. Shvec V.F., Makarov M.G., Luganskii A.I., Gorbunov A.V., Suchkov Yu.P., Staroverov D.V.,  Digurov N.G. Mathematical model of thermo-oxidative cracking tar // Himicheskaya promishlennost segodnya [Chemical Industry Today].  2012.

no. 7. pp.51-53. (in Russ).

Engineer technique for vortex chamber with weighted liquid drop layer

Vitaliy V. Kharkov

Kazan National Research Technological University, Department of Food Production Equipment, Assistant Professor. Address: 68 Karl Marx street, Kazan, 420015, Republic of Tatarstan, Russian Federation. Tel: +7 (843) 231-43-07,

e-mail:  v.v.kharkov@gmail.com

Andrey N. Nikolaev

Kazan National Research Technological University, Head of Department of Food Production Equipment, Doctor of Engineering, Professor. Address: 68 Karl Marx street, Kazan, 420015, Republic of Tatarstan, Russian Federation.

Tel: +7(843) 231-43-07, e-mail:  andr_nik_nik@rambler.ru

Keywords: swirling flow, tangent swirl diffuser, thermolabile solution.

Vortex-type equipment can be used for heat concentration of thermolabile materials in the “gentle” mode, providing indestructibility of matter. Special traffic flow management as drop rotating weighed layer provides lack of direct contact with heated surface of chamber responsible for activation thermal destruction processes. The main problem for this type apparatus is a variety of factors and the aim of the study is to construct the real technique reflecting industrial application, specifics of design features, operating mode, and internal processes. Based on aerohydrodynamics principles of swirling flows and on condition that all size drops are weighed, authors obtained the analytical equations including constructive the characteristics of vortex chamber and gas tangent blade swirling diffuser, the technological regime properties. Using the relations in the range of the recommended values for major parameters as the base, the engineer charts applicable to the vortex chamber for thermolabile liquids concentration are constructed.

References

1.	Smulsky J. J. Actual mathematical problems and thorny way of science, Put' nauki, 2015, no. 10 (20), p. 10-38 (in Russ.).

2.	Yershin Shakhbaz A., Paradoxes in Aerohydrodynamics // Springer International Publishing, 2017.

3.	Patent RU no. 156401. Vortex camera for liquid food concentration in swirling gas flow. Kharkov V.V., Nikolaev A.N., Bull. no. 31, 2015.

4.	Kharkov V. V., Nikolaev A. N. Numerical researches of drop mechanical trajectory in vortex apparatus for concentrating fruit juices, Vestnik Kazanskogo tehnologicheskogo universiteta, 2014, Т. 17, no. 16, p. 191–193 (in Russ.).

5.	Kharkov V. V., Ovchinnikov А. А., Analysis of forces defining drop dynamics in swirling gas flow, Vestnik tehnologicheskogo universiteta, 2015, Т. 18, no. 9, p. 106–109 (in Russ.).

6.	Kharkov V. V., Nikolaev A. N. Distinctive features of weighted liquid drop layer formation in the vortex chamber for the juice concentration. 5th International Conference Heat and Mass Transfer and Hydrodynamics in Swirling Flows, Kazan. 19–22 October 2015 // St. Petersburg: Svoe izdatelstvo, 2015, pp. 76–77 (in Russ.).

7.	Ovchinnikov A. A. Dynamics of swirling turbulent flows in vortex separators. // Kazan: Novoe znanie, 2005 (in Russ.).

8.	Bird R., Stewart W., Lightfoot E. Transport Phenomena. // М.: Himia, 1974 (in Russ.).

9.	Nikolaev N. A., Ovchinnikov А. А., Malusov V. А., Gavoronkov N. М. Drop breaking principles of liquid in vortex contact devices for mass-transfer apparatus, Izvestia VUZov. Himiya i him. tehnologia и хим. технология, 1976, Т. 19, no. 11, p. 1772–1776 (in Russ.).

Development of mathematical model of the process of biodiesel epoxidation in the presence of a molybdenum catalyst

Yudaev Sergey Alexandrovich

Tomsk Polytechnic University, Department of Chemical Technology of Fuel and Chemical Cybernetics, post-graduate student. E-mail: udgin92@mail.ru

Ivashkina Elena Nikolaevna

Tomsk Polytechnic University, Department of Chemical Technology of Fuel and Chemical Cybernetics, Professor, Dr.Sc.. E-mail: ivashkinaen@tpu.ru

Dolganova Irena Olegovna

Tomsk Polytechnic University, Department of Chemical Technology of Fuel and Chemical Cybernetics, Researcher, Ph.D. E-mail: dolganovaio@tpu.ru

Kulazhskaya Anna Dmitrievna

Russian Chemical and Technological University. D.I. Mendeleyev, Department of Chemical Technology of basic organic and petrochemical synthesis, post-graduate student. E-mail: kulazhskaya_92@inbox.ru

Sapunov Valentin Nikolaevich

D.I.Mendeleyev University of Chemical Technology of Russia, Professor of the Department of Basic Organic and Petrochemical Synthesis Technology. E-mail: sapunovvals@gmail.com

Keywords: fatty acid methyl esters (FAME), biodiesel, epoxidation, quantum-chemical methods, mathematical model.

Experimental data on oxidation of methyl esters of fatty acids of vegetable oils (sunflower, rape and olive oil) by air oxygen were given. Experiments were made in the columned device in the presence of the epoxidation catalyst – compound of propylene glycol and molybdenum. The main products of reaction were the corresponding epoxides which are formed on several ways during  catalytic epoxidation of nonsaturated fragments of the oxidized by air from the formed peroxyradicals and hydroperoxides. The main contribution to thermal effect of the process is made by reactions of oxidizing destruction at a rupture of double connection with formation of aldehydes. The scheme of process of oxidation and epoxidation of methyl air of fatty acids of vegetable oils and its mathematical model with use of quantum and chemical methods of calculation of thermodynamic functions for the main and side reactions with the analysis of the experimental data obtained as a result of carrying out process on different types of raw materials were offered. The main regularities of process of epoxidation are revealed. An inspection of adequacy to the developed model was carried out.

References

1.	G.P., Moss. Glossary of class names of organic compounds and reactive intermediates based on structure. International union of pure and applied chemistry,1995, no.67, pp.1307-1375.

2.	Goldberg M.M. Raw materials and intermediates for paint and varnish materials. M.: Chemistry, 1978, 512 p. (In Russ)

3.	Chemical products. FKP Plant named after Ya.M. Sverdlov. [Electronic resource]. - Access mode: http://www.sverdlova.ru/production/chemical/ (In Russ)

4.	Voronov M.S., Sapunov V.N., Kulazhskaya A.D., Gustyakova S.I., Kozeeva I.S., Kaleeva E.S., Yazmukhamedova I.M., Regularities of formation of formic acid in aqueous Solutions of hydrogen peroxide and formic acid. Chemical Industry today, 2016, no.5, pp.7-15 (In Russ)

5.	, Kazemizadeh Mohammed R; McKinney Timothy E; Epoxidized composition and methods for making the same. WO2012019073, 2012.

6.	Kulazhskaya A.D., Sapunov V.N., Voronov M.S., Makarov A.A., Kaleeva E.S., Amirkhanov I.R., Kustov A.A., Makarova E.M., Kuznetsova I.V., Suchkov Yu.P,, Method for the epoxidation of organic compounds. RU 2016123769, 2016 (In Russ)

7.	I.M., Rizwanul Fattahn. Effect of antioxidants on oxidation stability of biodiesel derived from vegetable and animal based feedstocks. Renewable and Sustainable Energy Reviews, 2014, no.30, pp.356-370.

8.	Krylov I.A., Litvintsev I.Yu., Sapunov V.N. Kinetics and mechanism of liquid-phase oxidation of cyclohexene. Kinetics and catalysis. 1983, Volume XXIV; Issue. 1. pp. 47-52. (In Russ)

9.	Fraser, Bronston. Expanding the scope of gallium-catalyzed oleﬁn epoxidation. Polyhedron. 2016, no.5.pp.35-43.

10.	Chao, Chen. Size-selective epoxidation of oleﬁns in two new metal-organic framework constructed from six-coordinated tetranuclear Cu(II) SBUs. Microporous and Mesoporous Materials, 2016, no.232, pp.167-173.

11.	Hongcheng Gao Catalytic epoxidation of olefin over supramolecular compounds of molybdenum oxide clusters and a copper complex. // Chinese Journal of Catalysis, 2015, no.36, pp.1811-1817.

12.	Sajjad, Mohebbia. Oxovanadium(IV) complexes as homogeneous catalyst—aerobic epoxidation of oleﬁns. Applied Catalysis A: General, 2005, no.278, pp. 263-267.

13.	B., Tang. Co2+-exchanged SAPO-5 and SAPO-34 as efﬁcient heterogeneous catalysts for aerobic epoxidation of alkenes. Catalysis Communications, 2013, no.31, pp.42-47.

14.	18. Rubailo V.L. Liquid-phase oxidation of unsaturated compounds / VL Rubailo. And others. M.: Chemistry, 1989, 224 p. (In Russ)

15.	Jiayu, Xin. Kinetics on the oxidation of biodiesel stabilized with antioxidant. Fuel, 2009, no.88, pp.282-286.

16.	Ned, A. Porter. Unified Mechanism for Polyunsaturated Fatty Acid Autoxidation. Competition of Peroxy Radical Hydrogen Atom Abstraction, Scission and Cyclization. J. Am. Chem. SOC, 1981, no.103, pp.6441-6455.

17.	Ivashkina E. N. Investigation of the process of mixing reagents in the technology of alkylation of benzene with ethylene using the methods of computational hydrodynamics. Chemical Industry Today, 2014, no.8, pp.46-56. (In Russ).

18.	Pisarev M.O. Increase of the efficiency of the apparatuses of the technological installation of low-temperature gas separation with the use of an imitation dynamic model. Chemical Industry Today, 2016, no.5, pp.46-56. (In Russ).

19.	Tsyshevsky R.V., Garifzyanova G.G., Khrapkovsky G.М. Quantum-chemical calculations of the mechanisms of chemical reactions. Kazan: KNITU, 2012, 86 p. (In Russ).

Vortex rectification stages with low hydraulic resistance

Kustov Alexander Vladimirovich.

Siberian State Technological University,PHd, Associate Professor of the Department of Mechanics. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Tel. 8 (391) 2121914. E-mail: alexkust@rambler.ru

Shastovsky Pavel Sergeevich. Siberian State Technological University, senior lecturer of the Department of Mechanics. Address: 660049, Krasnoyarsk, Mira Ave. 82. Tel. +7(391) 2121914.

Goncharova Yana Sergeevna. Siberian State Technological University, Cand. Ped. Sci., Associate Professor of the Department of Structural Materials and Mechanical Engineering. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Tel. +7 (391) 2660420

Alashkevich Yuri Davydovich. Siberian State Technological University, Doctor of Science. Professor, Head of the Department of Machines and Apparatus of Industrial Technologies. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Tel. +7 (391) 227-86-19

Sergiyakova Yulia Timofeevna. Siberian State Technological University, student. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Vasilchenko Ekaterina Sergeevna. Siberian State Technological University, student. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Karelina Alexandra Alexandrovna. Siberian State Technological University, student. Address: 660049, Krasnoyarsk, Mira Ave. 82.

Keywords: rectification, the contact stage, downcomers device, hydraulic resistance.

The paper presents the developed vortex distillation stage with a low flow resistance in the complex processing of vegetable raw material processes (the production of ethanol, the separation of fluids used in the preparation of biologically active substances). Analysis of intensification mass exchange paths (i.e. the gas transfer into the liquid) show that the use for these processes bubbling devices did not significantly improve performance and efficiency. Therefore, the use of centrifugal acceleration is the easiest way of intensification of mass transfer. The rotation promotes fragmentation stream of gas bubbles at the contact level, mainly due to the force of inertia.

References

1. Voinov N.A., Nikolaev N.A., Kustov A.V., Tarovatui D.V. Hydrodynamics contact step with tangentional swirl. Khimicheskaya promyshnost segodnya [Chemical Industry today]. 2009.  № 6. Pp.36-43. 9 ( in Russ ).

2. Voinov N.A., Nikolaev N. A. , Kustov A.V. Hydrodynamics and Mass Exchange in Vortex Rectifying Column// Russian Journal of Applied Chemistry, 2009, Vol. 82, No. 4, Pp. 730-735

3. Voinov N.A., Pankov V.A., Kustov A.V.  Contact device for heat and mass transfer devices. RU 2355457, 2009. ( in Russ ).

4. Kustov A.V., Alashkevich Yu. D., Martunovskaya S.N., Bukelmanov. I.I.,  Shakuro A.R. Determination of the diameter of the gas ( steam ) bubbles swirl on stage at rectification. Khvoinye borealnoi zony [Coniferous boreal zone]. ( in Russ ).

5.  Kustov A. V. Hydrodynamics and mass transfer in the vortex of distillation steps in the processing of vegetable raw materials: Aftoreterat dissertacii na soiskanie stepeni kandidata nauk [Abstract. thesis ... Candidate of Science]. Krasnoyarsk: SibGTU. 2010. 22 p. ( in Russ ).

Determination of effective technological parameters of the apparatus for the separation of oil-water emulsions in an inhomogeneous electric field

Zaykovskiy Vsevolod Viktorovich, postgraduate student, department of transport and storage of oil and gas National Research Tomsk Polytechnic University. Address: 634050, Tomsk, Lenina ave, 30. E-mail: alkast@tpu.ru

Kharlamov Sergey Nikolaevich, Dr.Sc., full professor, Oil and Gas Transport&Storage  Department, National Research Tomsk Polytechnic University. Address: 634050, Tomsk, Lenin ave, 30. E-mail: kharsn@mail.ru

Keywords: water-in-oil emulsion, non-uniform electric field, dielectrophoresis, criterion of coalescence efficiency.

The article presents the results of researches about determination of effective structural parameters of electrode systems devices that implement the processing and separation of water-in-oil emulsion in an inhomogeneous electric field. The verification of the earlier proposed mathematical model provided using original data from experimental observation water-in-oil emulsion dynamics. The original criterion of the effectiveness of coalescence  of water droplets in oil that allowing to compare the effect of geometric parameters of the installation performance is proposed. In the study determined threshold value of the interelectrode distance and the length of the shortest electrode in the apparatus for treatment of water-in-oil emulsions in an inhomogeneous electric field.

References

1. Loginov V.I. Dehydration and desalting of crude oils. M: Chimia, 1979. 109 p. (in Russ.).

2. Panchenkov G.M., Tsabek L.K. Behavior of emulsions in external electric field. M.: Chimia, 1969. 190 p. (in Russ.).

3. Skoblo A.I., Molokaniv Yu.K., Vladimirov A.I., Schelkunov V.A. Processes and devices of refining and petrochemistry. M.: Nedra-Biznescentr, 2000. 677 p. (in Russ.).

4. Van Gerpen J. Biodiesel processing and production. Fuel Processing Technology, 2005, no.86, pp. 1097-1107.

5. L.L. Schramm. Emulsions, foams and suspensions. Weinheim: WYLEY-VCH, 2005. 465 p.

6. Levchenko D.N., Bergshtein N.V., Khudyakova A.D., Nikolaeva N.M. Emulsions of water and oil and methods for their destruction. M.: Chimia, 1967. 200 p. (in Russ.).

7. Boschee P. Advances in Electrostatic Treatment of Crude Oil. Oil and Gas Facilities, 2012, no.10, pp. 17-21.

8. Eow J.S., Ghadiri M., Sharif A.O., Williams T.J. Electrostatic enhancement of coalescence of water droplets in oil: a review of the current understanding. Chemical Engineering Journal, 2001, no.84, pp. 173-192.

9. Less S., Vilagines R. The electrocoalescers' technology: Advances, strengths and limitations for crude oil separation. Journal of Petroleum Science and Engineering, 2012, no.81, pp. 57-63.

10. Atten P., Lundgaard L., Berg G. A simplified model of electrocoalescence of two close water droplets in oil. Journal of Electrostatics, 2006, no.64, pp. 550–554.

11. Electrophoretically mediated partial coalescence of a charged microdrop. R. Pillai, J.D. Berry, D.J. Harvie, M.R. Davidson. Chemical Engineering Science,  2016, URL: http://www.sciencedirect.com/science/article/pii/S0009250916303888 (date of usage: 22.07.2016).

12. Electrocoalescence behavior of two identical droplets with various droplet radii. B.B. Wang, X.D. Wang, T.H. Wang, W.M. Yan. Applied Thermal Engineering, 2016, URL: http://www.sciencedirect.com/science/article/pii/ S1359431116307463 (date of usage: 21.05.2016).

13. Changhui G., Limin H. Coalescence behaviour of two large water-drops in viscous oil under a DC electric field. Journal of Electrostatics, 2014, no.72, pp. 470-476.

14. Li B., Zhiqian S., Zhenbo W., Youhai J., Yuxin F. Effects of high-frequency and high-voltage pulsed electric field parameters on water chain formation. Journal of Electrostatics, 2016, no.80, pp. 22-29.

15. Atten P. Electrohydrodynamics of Dispersed Drops of Conducting Liquid: From Drops Deformation and Interaction to Emulsion Evolution. International Journal of Plasma Evironmental Science & Technology, 2013, no.7, pp. 2-12.

16. Ponomarev V.G., Yokamis E.G., Mongait I.L. Purification of waste waters of oil refineries. M.: Chimiya, 1985. 255 p. (in Russ.).

17.	Ershov O.L., Zhigalin G.Ya., Kochurkov A.A., Polivanov A.N., Smulskii A.V., Storozhenko P.A. Method of dehydration of silicone fluids and device for its implementation. Ru №. 2350373, 2009. (in Russ.)

18. Mhatre S., Thaokar R. Electrocoalescence in non-uniform electric fields: an experimental study. Chemical Engineering and Processing: Process Intensification, 2015, no.96, pp. 28-38.

19. Chen Z., Shen X. Study on dielectrophoretic deposition of airborne particles in a vertical micro channel. Building and Environment, 2010, no.45, pp. 968-975.

20. Kharlamov S.N., Zaykovskiy V.V. Mathematical modelling of the effect of inhomogeneous electric field on the motion of drops of water in oil. Electronnii nauchnii zhurnal «Neftegazovoe delo» [Electronic scientific journal «Oil and gas business»], 2015, no.4, pp. 95-117 (in Russ.).

21. Zaykovskiy V.V., Kharlamov S.N., Muratov V.M. Experimental study of the motion of water droplets in water-oil emulsions during the separation in an inhomogeneous electric field. Izvestiya Tomskogo politekhnicheskogo universiteta. Inzhiniring georesursov [Bulletin of the Tomsk Polytechnic University. Geo Assets Engineering], 2016, no.10, pp. 22-35 (in Russ.).

22. Mhatre S., Vivacqua V., Ghadiri M., Abdullah A.M., Al-Marri M.J., Hassanpour A., Hewakandamby B., Azzopardi B., Kermani B. Electrostatic phase separation: A review. Chemical Engineering Research and Design, 2015, no.96, pp. 177-195.